## Slide 1
ECSE 371 V23.0
Operational Amplifiers
L. Sears

## Slide 2
AOL
+
_
VIN+
VIN-
Voltage-controlled voltage source where Vout = AOL (VIN+ -
and AOL ~∞
VIN- )
VOUT
+V Supply
-V Supply
Ideal Op-Amp Model

## Slide 3
The output of an op-amp will always act to drive the differential input voltage to zero.
2. The inputs of an op-amp draw zero current.
3. Notwithstanding #2 above, the inputs of an op-amp or comparator must always be provided with a DC current path.
4. Remember that the output of an op amp is a voltage source that can both source and sink current.
All you need to know !!* :
BASIC OP-AMP CIRCUIT CONFIGURATIONS:
#1 above is a result of the op-amp’s extremely high gain and the presence of an external negative feedback network.
Op-Amp Fundamentals
*perhaps a slight exaggeration.
3
(Vout =Vin)
DIFFERENTIAL AMPLIFIER
Vout =
(ΔVin)R2/R1
Notes: Pertaining to this slide there will be a long, detailed discussion of op amp operation, applications, requirements, etc. Later in this topic a 741 data sheet could be shown.

## Slide 4
Closing the Loop
Negative feedback is one of the most valuable concepts in electrical engineering. If we start with a very high-gain amplifier and feed a fraction of the output back to the negative input of the amplifier, the gain of the amplifier is reduced to a value that is determined by the ratio of the feedback components, and not by the op-loop gain of the op amp.
By using the amplifier in the closed-loop configuration, we sacrifice gain but, in return, we dramatically improve performance of the amplifier.
The proportional improvement in amplifier performance can be approximated by the value of the Loop Gain:
Loop Gain = Open Loop Gain / Closed Loop Gain
Example: an op amp has an open-loop gain of 105 and a closed-loop gain of 100. The bandwidth of the closed-loop circuit will be 1000 times the open-loop bandwidth. In the closed-loop configuration, the gain will start rolling off at 10 kHz instead of the 10 Hz roll off exhibited by the open-loop gain.
BUT: You must remember that all parameters which depend upon loop gain, i.e. gain stability, linearity, etc. - will degrade at high frequencies because of the inevitable roll-off in the loop gain.
Closing the loop does not improve:
Input Offset Voltage
Input Bias Current
Large-Signal Output Current Slew Rate
Closing the loop improves:
Gain Stability and Linearity
Bandwidth
Distortion
Linearity
Noise
Input and Output Impedances
OR, the percentage gain error E% = 100ACL/AOL

## Slide 5
fc (cutoff frequency) is the frequency at which the closed-loop gain (Acl) begins dropping (3dB down): fc = GBP/Acl
The blue trace in the above graph shows the gain as a function of frequency of a particular op amp when it is operating open-loop; in other words, there is no feedback. The open loop gain drops very rapidly, starting around 10 Hz. The gain continues to drop at a rate of 20 DB per decade until, at some high-frequency, it reaches a gain of one. This frequency is known as the Gain Bandwidth Product and is specified, in Hz, for all op amps.
The red dotted line indicates the frequency response of the same op amp used in a circuit that has a closed-loop gain of 100. In this case, as long as the closed-loop gain is much less than the open- loop gain, the closed- loop gain will be determined only by the passive components in the feedback loop. Therefore, the closed loop gain will remain constant (but at a lower value) until the open-loop gain has dropped to where it approaches the closed loop gain. This point is known as the cutoff frequency, fc. At frequencies greater than fc, the closed- loop gain will equal the open-loop gain.
Slope =
-20dB/decade
Note that this relationship is only valid for small signals. At large output swings, slew rate may limit effective frequency response.
Op-Amp Frequency Response
Open loop response is shown in blue. Closed-loop response, with gain = 100, is shown in red:
106
105
104
103
102
101
100
Open Loop Gain
dB
Vout/Vin
120
100
80
60
40
20
0
Frequency, Hz
Op-Amp Open-Loop Gain
Op-Amp Closed-Loop Gain
Feedback Sets Gain = 100
GBP = 106 Hz.
fc
106
(GBP is a datasheet spec)

## Slide 6
Some of the more important op amp specifications are discussed below (with some simplifications). If we could buy “ideal” op-amps, we would not, of course, have to worry about any of these things. Since we can’t, these are some of the items to keep in mind:
1. Open Loop Gain, AOL No units
This is the DC gain of the op-amp without any feedback. It is simply the ratio of the output voltage to the input voltage. It is a ridiculously large number, typically 100,000 or more, so we usually give up and simply say it’s really big. The fact that this number is so large is what results in the simple equations that determine closed-loop gain –which is established only by resistor values. These equations are approximations, but as long as the open-loop gain is much, much larger than the closed-loop gain, these equations are accurate to a fraction of 1%
The open-loop gain, AOL, is defined at DC because, unfortunately, it drops quickly as frequency increases. In the case of a general-purpose op amp such as the 741, AOL will decrease from about 100,000 to about zero when the frequency reaches one megahertz. Yes, really. The rule- of- thumb is that at DC and low frequencies, the open-loop gain will be so high that we can ignore its value. However, at higher frequencies (even starting with audio frequencies), AOL becomes very important because it decreases dramatically.
3. Input Resistance, ri Ohms
This is the ratio of the input voltage to the input current. Ideally, this value is infinite, but most op-amps have typical values in the order of megohms (and will be multiplied by the loop gain). You and I will be perfectly happy if you ignore this specification and simply assume that input impedance is infinite. Remember, however, that input bias current is unrelated to input resistance and can be very important. See below.
4. Output Resistance, ro Ohms
This is the series resistance of the output voltage source. It is typically a few hundred ohms, but it is generally reduced by the loop gain. This means that the series impedance of the output will be vanishingly small, perhaps a few ohms. As in the case of input resistance, it is best ignored. So please assume that this value is zero and get on with your life. Note, however, that this is a small-signal parameter and only applies to extremely small output swings (typically millivolts); it does not mean that the output of the op-amp is immune to loading. The ability of the op amp to provide current is determined by the short circuit current, ISC
5. Input Bias Current, IIB uA or nA
Both op-amp inputs must be connected to “something” to provide a DC path for IIB; this is necessary for operation. Although this current is zero for an ideal op-amp, and is generally quite low in a real op amp, in certain situations it is an extremely important specification.
6. Bandwidth, GBP KHz or MHz
The bandwidth of an op-amp is the allowable range of frequencies that it can amplify. An ideal op amp has infinite bandwidth, and so it can amplify any signal from DC to the highest AC frequencies. Real op-amps, however, experience a reduction in their open-loop gain as described above. Therefore, at high frequencies the open-loop gain will no longer be much higher than the closed-loop gain, so the closed-loop gain will not be determined by the resistor values and will drop in value. The parameter Gain Bandwidth Product (GBP) is used to describe the limit of the bandwidth of an op-amp. It is equal to the frequency at which the open-loop gain of the amplifier becomes unity.
Op-Amp Specifications 1/3
6

## Slide 7
Op-Amp Specifications 2/3
7. Slew Rate, SR v/usec
The slew rate of an op amp is the maximum rate of change in the output voltage caused by a step-change in the input. It is measured as a voltage change in a given time— usually V/µs. Ideally, the slew rate of an op amp should be infinite, thus allowing the output to be an exact amplified copy of the input, without any distortion. The higher the value of slew rate, the faster the output can change and the more accurately the op-amp can reproduce rapidly changing waveforms. Note that slew rate is independent of GBP and is an additional factor that may contribute to poor high-frequency performance.
● To operate at a frequency of f: f < (SR / 𝛑Vp) where Vp is the output amplitude.
8. Input Offset Voltage, VIO uV, mV
This is the maximum differential voltage needed at the input to get a 0V output; ideally the output is zero when both inputs to the op amp are zero. Although offset voltages are generally quite small (sometimes under one millivolt,) they add or subtract from the input voltage and maybe the troublesome in high-gain DC amplifiers.
9. Single Supply or Dual (split) Supply
Op amps require a fixed power supply which is not related to the signal voltage; two terminals are provided to make this connection. In a single-supply configuration (A), the positive and negative terminals of the op-amp are connected across the supply; the negative side of the supply is sometimes referred to as common, or ground. In a dual- supply configuration (B), the power supply sources are connected in series, and the center connection is referred to as common or ground. The top and bottom supply connections are often referred to as “rails”. Notice that the op-amp does not have a ground terminal. The input (signal) voltage is a voltage source that has one terminal connected to ground. The output voltage is also measured (or “referenced) with respect to ground.
-
-
(A)
By connecting the circuit’s “ground” to the center point (common) of the supplies, the amplifier will be biased so that, with zero input voltage, the output will also be at ground. Circuit ground is the point to which input sources, output loads, and measurement equipment are usually connected. With dual supplies, both inputs and outputs can swing both positive and negative with respect to ground. This is sometimes necessary for AC signals such as audio.
(B)
A “single-supply” op-amp uses the negative rail as ground. Therefore, it is necessary to carefully configure circuits to be used with AC signals, since the amplifier inputs cannot accept negative voltages (negative with respect to ground). Also note that with a single supply there is no way for the output to swing below ground, so negative output voltages are not available. Single supplies are less expensive and more convenient than dual supplies, but require careful design when handling AC signals.
4
Feedback and input resistors are not shown.

## Slide 8
8. Power Supply Voltage V
Op-amps are available in a wide range of supply voltages, ranging from 1.8V to +/-20V or more. Power- supply current (not counting load current) can be as low as 1 µA in special, premium op-amps.
9. Output Voltage Swing Vpk or Vpp
The output of an ideal op-amp would be able to swing from ”rail to rail”. In other words, the maximum output voltage would be equal to the positive supply voltage in the positive direction, and the negative supply voltage in the negative direction. Real op-amps, however, are generally limited in their output voltage swing. Many older, split-supply op-amps, for example, can only reach to within a volt or two of the positive and negative rails. Op-amps designed for a single supply, however, will generally swing to within a fraction of a volt of the negative rail; in the positive direction, however, they may not swing very close to the positive rail.
10. Output Current Capability mA
In many cases, such as driving a loudspeaker or a motor, it may be important for an op-amp to supply a significant amount of current. However, many op-amps are limited to sourcing or sinking output current in the range of 20 mA, so some sort of power amplifier may be required. Newer op-amps designed for low current and low-voltage operation may be very limited in output-current capability. They may be advertised as “rail to rail output”, but they can only provide such a large voltage swing under extremely low-load conditions.
Note that almost all op-amps feature some degree of short-circuit protection; this means that the output current is current-limited (and will appear to be a constant-current source) in case it is inadvertently connected to ground. It is important to remember, however, that even under current-limited conditions, power dissipation in the op-amp can be large and destructive! Under conditions of a short circuit to ground, dissipation will equal the output current times the voltage of the power supply that is supplying the current.
11. Input Voltage Range V
There are strict limitations on the magnitude of the voltage that may appear on the op-amp signal inputs. There are limited number of op amps that advertise “rail to rail input”. But generally, the input voltage range of older, split-supply op amps is limited to within a few volts of the positive and negative rails. However, the input voltage, of some older, popular, single-supply op-amps must be limited to within a few volts of the positive rail and must never go below the negative rail. With designs that require wide excursions of the input voltage, careful attention must be paid to input voltage limits; unexpected, bizarre, op-amp behavior may otherwise occur.
12. ABSOLUTE MAXIMUM RATINGS V, A, PD, T
These parameters are listed at the beginning of every data sheet, and specify maximum allowable voltage, current, power dissipation, and temperature limits. Exceeding these values, even briefly, may cause permanent damage to the device. They aren’t kidding!
Op-Amp Specifications 3/3
5
Notes: Discuss compromises. For example, GPB versus power consumption nand, of course, because.

## Slide 9
There are a lot of specifications, but which ones are really important? Of course, there is no simple answer, and if there were you wouldn’t need to take this course. The choice of an op-amp depends upon all kinds of variables, including the details of your application, availability of parts, and cost. But here are the most important things to consider (these are not hard-and-fast rules, however):
1. The first issue to consider is probably power supply voltage and the important matter of single supply or dual supply operation.
2. Always ignore the input resistance and output resistance specifications of the op amp. On the other hand, the input resistance and output-current capability of your complete op amp circuit are extremely important; but these are unrelated to the input resistance and output resistance specifications of the op amp itself.
3. For a quick-and-dirty DC application (including frequencies less than 10 KHz), after considering the power supply you can often ignore everything else on the list of specifications (whew !).
4. The 2 parameters that will probably be the most troublesome and may cause unexpected problems, will be input bias current and frequency response issues. High input bias current can produce offset voltages when high values of resistance (>50KΩ?) are present at the op-amp inputs. This offset voltage, produced by the input bias current, is usually more of a problem than the op-amp input offset-voltage specification.
Always be alert to the fact that, at frequencies greater than a few KHz, frequency rolloff may occur If the closed-loop gain is high. At higher frequencies you must consider the reduction in open-loop gain and the limitation in output voltage swing due to slew rate.
5. Don’t forget that even though the closed-loop output resistance of an amplifier will be essentially zero, the output of the op amp is still current-limited - typically to 20 mA or so.
Op-Amp Specifications, Discussion
5
Closing the loop does not improve:
Input Offset Voltage
Input Bias Current
Large-Signal Output Current Slew Rate
Closing the loop improves:
Gain Stability and Linearity
Bandwidth
Distortion
Linearity
Noise
Input and Output Impedances
Notes: Discuss compromises. For example, GPB versus power consumptionand, of course, because.

## Slide 10
OP AMP APPLICATION EXAMPLES
Requires a resistor from Vout to ground.

## Slide 11
OP- AMP INPUT CHARACTERISTICS
Input Offset Voltage
The inputs of an ideal operational amplifier will be perfectly symmetrical and matched. As a result, the output of the op-amp should be zero when both inputs are zero. However in a real op amp, it is always necessary to apply a slight positive or negative voltage to one of the inputs to produce a zero output-voltage. The small trimming voltage necessary to produce a zero output-voltage is called the input offset voltage, Vos
Op amps are available with offsets ranging from a few microvolts to several millivolts. Offset voltage changes with temperature. Depending on the specific part number, the offset voltage temperature coefficient varies from several nV to several uV per oC, and can be either positive or negative. Some operational amplifiers provide pins so a potentiometer can be connected to trim the offset voltage. However, you are usually better off simply buying a higher quality op-amp with a lower offset voltage.
The effect of offset voltage in a particular circuit may or may not be critical. For example, the output of an AC amplifier may be capacitor-coupled; as a result, offset voltages have little effect. However, a precision DC amplifier designed to operate with millivolt input signals will generally require an op-amp with a very low offset voltage.
Input Bias Current
The input of an ideal operational amplifier looks like an open circuit. Therefore, no current should be flowing in either input. In a real operational amplifier, a small current, known as the input bias current, Ib, flows in each input and is required to make the op amp function. Therefore, both inputs must be provided with a DC path. The direction of this current may be into or out of the input, depending on the type of op amp.
Since the input of an op amp is designed to be perfectly matched and symmetrical, we would expect Ib to be equal in both leads. However, due to errors in matching, the bias currents may be quite unequal. In the case of MOS op amps, the bias currents (which are actually leakage), whereas extremely small, may actually flow in different directions. The difference in bias currents is called the input offset current.
For bipolar and FET op-amps, where the bias currents in each input are in the same direction, Ib Is defined as the average of the two bias currents. For MOS op-amps the definition of Ib is vague because the bias currents may be in opposite directions, but the published value is usually the maximum of the two values.
Input bias current flowing through external resistances at the input of an operational amplifier will produce voltage drops at the op-amp inputs which will appear as an input offset voltage. If resistances are high, these offsets can be very significant. To minimize voltage offsets due to bias current, the resistance driving both inputs should be as low in resistance as possible and approximately equal in value. (For example, in the case of a non-inverting amplifier, the resistance in series with the positive input should be approximately equal to the parallel combination of Rf and R1. It may be necessary to add resistance to the positive input to obtain this balance.) Note, however, that if input offset current is high, or temperature changes are great, balancing the external input resistances may not be completely effective in minimizing circuit offset voltage.
And now, a deeper dive....

## Slide 12
Speaking very generally, when designing a precision DC amplifier with high resistances at the inputs, bias currents are more important than offset voltages - especially at high temperatures and with FET or MOS op-amps.
It would seem that an FET or MOS-type of op-amp would always the best choice for applications requiring low bias current. However, whereas the bias current of a bipolar op-amp decreases by a factor of two with a 50 oC increase in temperature, the bias current of an FET or MOS-style op-amp increases by a factor of two with only a 10°C increase in temperature. Therefore, at high temperatures a bipolar op amp may have a far lower input bias current than the other types.
Input Voltage Limits
Operational amplifiers are very sensitive to input voltage limits. Exceeding the allowable input voltage may cause latch-up, phase reversal, or other strange and fatal consequences. The common mode input voltage range is the maximum voltage, with respect to ground, that can be applied to either or both inputs. The differential input voltage is the maximum voltage that can be applied across the inputs. In closed-loop operation this voltage should be zero, but due to op-amp response time or other transient conditions large differential voltages may occur.
Some Op amps have protection diodes across the positive and negative inputs. These diodes limit the maximum input differential voltage to about 0.5 V. When operating as an op-amp the differential input voltage is zero (as long as the loop is closed and the circuit is operating properly). However, in certain applications the differential input voltage can be large and these diodes may cause difficulties.
Bias Current Comments:
The bias current of a bipolar op amp with NPN inputs (741) flows INTO the op-amp and DECREASES with temperature.
The bias current of a bipolar op amp with PNP inputs (324) flows OUT OF the op-amp and DECREASES with temperature.
The bias current of an FET op-amp flows out of the op-amp and INCREASES dramatically with temperature.
The bias current of an CMOS-style op-amp is due to leakage current and may flow in either direction. The positive and negative inputs may even have bias currents flowing in opposite directions. The bias current INCREASES dramatically with temperature.




Op-Amp Selection for Bias Current:
Bipolar op-amps usually have input bias currents in the range of 10-100 nA.
FET op-amps usually have input bias currents in the range of 1-10 nA.
MOS op-amps usually have input bias currents in the pA range.



OP- AMP INPUT CHARACTERISTICS, continued

## Slide 13
AC CHARACTERISTICS
Frequency Response
The ability of an op-amp to amplify high frequencies is characterized by its bandwidth. The op-amp is constructed of several stages that provide extremely high voltage gain; this is called the open loop gain or Aol. However, this voltage gain varies dramatically from part the part and with temperature. It's most notable characteristic, however, is that it drops rapidly as frequency increases. Whereas the gain at very low frequencies may be 105 or 106, it will drop to a value of one at some very high frequency; this frequency is called the Gain Bandwidth Product, or GBP, and is listed on the op-amp data sheet. This is a small signal parameter, valid only with small signal swings.
Using an op-amp in the open-loop configuration is generally useless because of this gain variation. However, adding negative feedback and operating in a closed-loop configuration will sacrifice much of the open-loop gain in return for stable gain over a wide bandwidth.
Adding negative feedback will also improve other parameters such as small-signal input and output resistance. However, the most important improvement is usually gain stabilization.
OP- AMP OUTPUT CHARACTERISTICS
DC CHARACTERISTICS
Voltage Swing
The output of an ideal op-amp is a voltage source that can both source and sink current, swings from rail-to-rail, and provides infinite current. The output of a typical real op-amp can only source and sink tens of milliamps before it is current-limited. Some op-amps have an output swing approaching rail-to-rail, but only when supplying very low currents; read the data sheet very carefully. Note that the load is usually connected to ground but may be connected to either rail.
Op-amps have output series resistance of a hundred ohms or so. However, for small signal operation this is almost always irrelevant because the incorporation of negative feedback dramatically reduces the output resistance of an amplifier.
Large Signal (DC) Limits on Op-Amp Voltage Swing
The ability of the op-amp output to drive a load is limited, among other reasons, by its ability to source and/or sink current - as described above. At heavy loads, current limiting will limit the output voltage swing. This limit is specified as short-circuit current on the op-amp data sheet. At higher supply voltages, power dissipation in the op amp may cause overheating leading to damage or over temp shut down. Also note:
∙ Most op-amps specified for single-supply operation will swing very close to the negative rail.
∙ Some op-amps designed specifically for dual supplies will not swing too close to either rail.
∙ Op-amps specified as “rail-to-rail” output will not do so when loaded even slightly.

## Slide 14
Slew Rate
The slew rate SR of an op-amp measures the ability of its output to quickly change in response to a step function. Slew rate is a large-signal characteristic and is not directly related to the frequency response of the internal amplifier stages. Slew rate is usually measured at unity gain by applying a square wave and driving the amplifier so its output swings close to the rails. When slew rate is limiting the output swing, the rise and fall times will have linear ramps; at very high frequencies, an input square wave will be converted to a triangular waveform. When responding to an input step function, internal capacitances in the op-amp are charged and discharged by current sources; therefore, the output will be seen to “slew” with characteristic, linear rise and fall slopes as it attempts to respond.
Although a limited slew rate is an obvious problem when amplifying a step function, a low slew rate will cause distortion of any signal waveform. For example, a sine wave will start to appear triangular, and its peak-to-peak amplitude will be limited, if the slew rate is not adequate.
 In order to output a sine wave with the proper amplitude and limited distortion:
f < SR / 𝛑Vp where f is the signal frequency, Vp is the amplitude, and SR is slew rate in V/usec.
To obtain adequate output signal swing at higher frequencies, close-loop frequency response and slew rate must be taken into consideration. If a heavy load is involved, current limiting and power dissipation must also be evaluated.
OP- AMP OUTPUT CHARACTERISTICS, continued

## Slide 15
Absolute Maximum Ratings are listed at the beginning of every data sheet, and specify maximum allowable voltage, current, power dissipation, and temperature limits. Exceeding these values, even briefly, may cause permanent damage to the device. These parameters do not represent allowable operating conditions.
You must NEVER operate at or near these conditions! They aren’t kidding!
Note that there is no Absolute Maximum Rating for output current. Device failure will occur due to excessive junction temperature, which can occur as a result of power dissipation in the device. Junction temperature is related to output current, output voltage, supply voltage, duty cycle, and thermal resistance. Output current will be limited, by internal circuitry, to the short-circuit current specification, but excessive dissipation can easily occur due to the other factors.
OP-AMP “ABSOLUTE MAXIMUM RATINGS”
And finally, a very important note: With their very high gain, op-amps may randomly or erratically oscillate under certain conditions, especially if power is supplied via long leads, or it is late at night and your project is due in the morning. It is always necessary to bypass the power supply(ies) with a suitable capacitor(s) to ground.